ARCHITECTURAL SPECIFICATIONS

I/O CONTROL INTERFACE

ICSLan Input/Output Interface (FG2100-21)

DESIGN

- ICSLan Device Control Interface allow users to manage devices remotely from an AMX Central Controller over a standard Ethernet network.

- Practical solution for conference rooms, classroom or auditoriums where a single controller is used to manage multiple devices such as projectors spread throughout a facility or to add additional ports to an AMX Central Controller.

- I/O Control Interface shall employ Native NetLinx Technology making it simple to add expansion to an AMX installation. I/O Control Interfaces that do not employ Native NetLinx Technology shall not be accepted.

- I/O Control Interface must include Standard, Ethernet-Based Interface using familiar installation methodology utilizing standard switches rather than proprietary distribution hardware. I/O Control Interface Devices that do not include a standard, Ethernet-Based Interface shall not be accepted.

- I/O Control Interface must be powered over Ethernet. I/O Control Interface devices that are not powered over Ethernet shall not be accepted.

- I/O Control Interface includes one (1) ICSLan 10/100 Ethernet port.  I/O Control Interface devices that do not include one (1) ICSLan 10/100 Ethernet port shall not be accepted.

- I/O Control Interface must include at least eight (8) I/O Ports that may be configured for input or output functionality independently.  Output function must provide for an open-collector output to a common ground.  Input function must sense contact closure or 0-28 VDC voltage sensing.  I/O Control Interface devices with less than eight (8) I/O ports or do not meet the other requirements above shall not be accepted.

TECHNICAL SPECIFICATIONS

- Power requirements: PoE - Typical power draw: 1.9 Watts

- Dimensions: 1" x 4 3/8" x 5 1/8" (2.5 cm x 11.1 cm x 13.00 cm) (1 RU)

- Weight: 1 lb. (454 g)

- Enclosure: Steel, black powder coated finish

- Eight Input/Output channels

- STATUS LEDs

  - 1 Green LED shows connection and power status

  - 1 Green LED shows Ethernet Link status and activity

  - 8 Yellow LEDs (1 per I/O) show Input/Output activity

- CONNECTIONS / WIRING

  - 1 RJ-45 ICS-LAN Ethernet Connector

  - 1 10-Pin 3.5mm captive-screw terminal

OPTIONAL ACCESSORIES

- NXA-ENET8POE Gigabit Ethernet Switch

- PS-POE-AF PoE Injector

- AVB-VSTYLE-SURFACE-MNT V-Style Module Surface Mount

- AVB-VSTYLE-RMK-1U V-Style Module tray

- AVB-VSTYLE-RMK-FILL-1U V-Style Module tray with filled plates

- AVB-VSTYLE-POLE-MNT V-Style Module Pole Mount