AMX Metreau 6-Button Ethernet Keypad with Navigation

MET-6NE-WH (FG5793-01-WH), White Keypad 
MET-6NE-BL (FG5793-01-BL), Black Keypad

ETHERNET KEYPAD REQUIREMENTS

SUMMARY

- Keypad shall combine multiple tactile control surfaces into an aesthetically-pleasing and logically-laid out interface. Keypad shall be designed to be approachable, allowing users to easily and intuitively access multiple system functions.

COMMUNICATION REQUIREMENTS

- Keypad shall support Ethernet communications via a 10/100 port with industry standard RJ45 connector. Keypads supporting only proprietary communication protocols, or not supporting standard 10/100 Ethernet communications and connectors shall not be accepted.

- Keypad shall support daisy chaining of an additional (2) expansion keypads, providing power and communications to all keypads, while utilizing only single IP address for all keypads. Keypads not capable of daisy chaining at least (2) expansion keypads to provide power and communications to expansion keypads in the same manner shall not be accepted.

- Keypad shall be equipped with an integrated infrared (IR) Sensor capable of detecting 38 KHz (IR) pulses. Keypads without an integrated IR sensor, or with an integrated IR sensor not capable of detecting 38 KHz IR pulses, shall not be accepted.

POWER REQUIREMENTS

- Keypad shall be powered over Ethernet, adhering to the 802.3af standard. Keypads not powered over Ethernet, or not adhering to the 802.3af standard shall not be accepted.

TACTILE SURFACE REQUIREMENTS

- Keypad shall be equipped with a combination of (6) push-buttons and (1) navigation wheel with (1) center push-button. Keypads excluding a navigation wheel, or not providing the same combination of push-buttons and a navigation wheel, shall not be accepted.

- Keypad navigation wheel shall freely turn to allow clock and counter-clock rotations. Keypads without a navigation wheel, or without a freely- rotating navigation wheel shall not be accepted.

- Keypad push-button silk screen labels shall be customizable with up to (8) alphanumeric characters. Keypads with fixed button configurations, or not supporting custom silk screen labels with at least (8) alphanumeric characters shall not be accepted.

FEEDBACK REQUIREMENTS

- Keypad shall be equipped with buttons capable of providing visual feedback via integrated LED lights. Keypads not capable of providing visual feedback via integrated LED lights shall not be accepted.

- Keypad visual feedback shall be distinctly programmable as on, off, or flashing. Keypads not capable of providing distinctly programmable visual feedback in the same manner shall not be accepted.

- Keypad shall be equipped with programmable 7 light LED bar. Keypads not equipped with a programmable LED bar, or with a LED bar without at least 7 lights shall not be accepted.

- Keypad pushbutton and light bar LED light brightness shall be adjustable so as to provide a proper level of backlighting, with a discernible on and off state. Keypads without adjustable feedback LED lights shall not be accepted.

MOUNTING REQUIREMENTS

- Keypad shall mount into a US standard, single-gang, electrical box. Keypads requiring a custom back-box shall not be accepted.

PRODUCT IDs

- The Ethernet Keypad shall be manufactured by AMX and shall be a Metreau MET-6NE-WH (White).

- The Ethernet Keypad shall be manufactured by AMX and shall be a Metreau MET-6NE-BL (Black).

About AMX
AMX hardware and software solutions simplify the implementation, maintenance, and use of technology to create effective environments. With the increasing number of technologies and operating platforms at work and home, AMX solves the complexity of managing this technology with reliable, consistent and scalable systems. Our award-winning products span control and automation, system-wide switching and audio/video signal distribution, digital signage and technology management. They are implemented worldwide in conference rooms, homes, classrooms, network operation / command centers, hotels, entertainment venues, broadcast facilities, and more.  ©2014 AMX. All rights reserved. Specifications subject to change.  17 June 2014.

AMX.com   |   800.222.0193   |   469.624.8000   |   +1.469.624.7400   |   fax 469.624.7153