ARCHITECTURAL SPECIFICATIONS

NXV-CPI

Control Phone Interface (FG2263-03)

DESIGN

- Solution for organizations that already have Cisco® IP phones and want to add capabilities to control lights, shades and other AV equipment in smaller rooms from a Cisco IP phone. The Control Phone Interface allows IP phone users to minimize their investment in a new infrastructure by transforming the IP phone into a Modero Virtual Touch Panel

- Control Phone Interface must support Power over Ethernet (PoE). Control Phone Interface’s that do not support PoE shall not be accepted

- Control Phone Interface must support control four (4) ways; touch screen, hard buttons, soft keys, and/or numeric key pads. Control Phone Interface’s that do not support control in four (4) ways shall not be accepted

- Control Phone Interface must include one (1) Ethernet LAN 10/100 PoE port. Control Phone Interface’s that do not include one (1) Ethernet LAN 10/100 PoE port shall not be accepted

- Control Phone Interface must include control four (4) LED indicators. Control Phone Interface’s that do not include four (4) LED indicators shall not be accepted

- Control Phone Interface must include one (1) reset pushbutton. Control Phone Interface’s that do not include one (1) reset push button shall not be accepted

- Control Phone Interface must include a web-based configuration interface.  Control Phone Interface’s that do not include a web-based configuration interface shall not be accepted

- Control Phone Interface must support Telnet communications via TCP/IP. Control Phone Interface’s that do not support Telnet communications via TCP/IP shall not be accepted.

- Control Phone Interface must be compatible with Cisco models 7965G and 7975G. Control Phone Interface’s that are not compatible with Cisco models 7965G and 7975G shall not be accepted

TECHNICAL SPECIFICATIONS

- AC Power requirements: PoE

- Weight: 1.45 lbs. (0.65 kg)

- Dimensions: 1.66" x 5.54" x 4.10" (4.216 cm x 14.07 cm x 10.42 cm) – (1RU)

- Enclosure: Metal black matte finish

- Operate at temperatures 32°F to 104°F (0°C to 40°C)

- Relative Humidity of 5% to 85% non-condensing

- Memory: 64 Mbytes RAM, 256 Mbytes Flash

- Compatible with Cisco models 7965G and 7975G

CERTIFICATIONS

- FCC Class B

- CE

- IEC60950

- RoHS

OPTIONAL ACCESSORIES

- PS-POE-AF: Power over Ethernet injector

- AC-DIN-CS3 DIN Rail Mounting Bracket

- AC-RK Accessory Rack Kit