Engineering Bulletin:

Firmware Upgrade Procedure For

Positrack Pan/Tilt Units

Last reviewed: February 20, 2001

Bulletin ID: EB000008

The information in this bulletin applies to:

AXB-PT10 (FG630-61)

AXB-PT30 (FG630-60)

DESCRIPTION

The firmware upgrade procedure for these products to version 2.00 and higher is not typical of other Panja devices.  The following steps must be followed for a proper upgrade:

1) Using Softrom, begin a download of the new application code.
2) Abort the download process after the first few bytes have been sent by pressing the escape key.
3) Power cycle the unit -- the unit should power up running the boot code.
4) After the self-test the boot version can be checked with Softrom.
5) If the boot version is anything other than 2.00, download boot version 2.00.
6) After a successful download of the boot code, the unit will automatically reset and begin running the new boot code (version 2.00).
7) Download the new application code (version 2.04).  After a successful download of the application code, the unit will automatically begin running the new application code (version 2.04).

8) At this point the application version can be checked with Softrom.